## Slide 1
Problem Statement & Objective
Adaptive 2D Systolic Array on PYNQ-Z2
Problem
Edge AI layers repeatedly multiply matrices and accumulate results.
Small or irregular shapes leave a fixed compute grid underused.
Data movement and FPGA routing constrain useful throughput.
Objective
Build exact signed INT8 acceleration with two parallel 16 x 16 engines.
Support active regions, zero padding and software tiling of larger matrices.
Verify correctness, timing and workload power before board release.
Notes: Project scope is matrix multiplication C = A x B, targeting edge AI workloads. Gesture recognition is an application integration, not a measured current-board performance result.
Evidence inspected on October 6, 2026:
C:\Users\adars\OneDrive\Desktop\adaptive_systolic_array_docs\PYNQ-z2\src\accel_dual_engine_top.sv
C:\Users\adars\OneDrive\Desktop\adaptive_systolic_array_docs\PYNQ-z2\PRD.md
C:\Users\adars\OneDrive\Desktop\adaptive_systolic_array_docs\PYNQ-z2\pynq\adaptive_gemm.py

## Slide 2
Proposed Solution
512 physical MAC lanes | Exact INT8 arithmetic | 100 MHz routed candidate
Engine 0
16 x 16 processing elements
110 DSP + 146 LUT MACs
Engine 1
16 x 16 processing elements
110 DSP + 146 LUT MACs
Arithmetic
Signed INT8 inputs; 20-bit tile accumulators; sign-extended INT32 output.
Adaptive execution
M / K / N up to 16 per tile. Active masks and zero padding handle tails; Python tiles larger matrices.
Shared data path
One AXI DMA; ping-pong true dual-port BRAM feeds both engines.
Notes: The current integrated top defaults to DSP_PE_LIMIT_0=110 and DSP_PE_LIMIT_1=110 and ACC_WIDTH=20. Each 16x16 engine has 256 physical MACs, of which 110 are DSP and 146 are LUT-based. 512 x 100 MHz = 51.2 GMAC/s is an ideal fully utilized arithmetic ceiling, not tile latency, sustained throughput or CPU speedup. The two colored grids are editable schematic PE allocations, not a physical placement map.
Evidence inspected on October 6, 2026:
C:\Users\adars\OneDrive\Desktop\adaptive_systolic_array_docs\PYNQ-z2\src\accel_dual_engine_top.sv
C:\Users\adars\OneDrive\Desktop\adaptive_systolic_array_docs\PYNQ-z2\src\accel_dual_tile_core.sv
C:\Users\adars\OneDrive\Desktop\adaptive_systolic_array_docs\PYNQ-z2\src\pe_mac.sv
C:\Users\adars\OneDrive\Desktop\adaptive_systolic_array_docs\PYNQ-z2\board_implementation\vivado\block_design.tcl
C:\Users\adars\OneDrive\Desktop\adaptive_systolic_array_docs\PYNQ-z2\pynq\adaptive_gemm.py
C:\Users\adars\OneDrive\Desktop\adaptive_systolic_array_docs\PYNQ-z2\results\power_optimization\dsp110_100_direct\timing_routed.rpt

## Slide 3
System Architecture & Workflow
Dual 16 x 16 engines | 512 MAC PEs | each engine = 110 DSP48E1 + 146 LUT PEs | 100 MHz
WORKFLOW
1
Input / CNN layer
image, feature map, weights
2
ARM / PYNQ
INT8 quantize, set M/K/N, tiling
3
DDR3
A, B input buffers
4
AXI DMA MM2S
32-bit stream, burst 16
5
BRAM
Bank 0 / 1 ping-pong
6
Engine 0 + 1
parallel compute, A/B skew, mesh
7
Capture
INT20 to INT32, 256 words/tile
8
AXI DMA S2MM
INT32 stream to DDR3
9
DDR3
C result buffers
10
PYNQ / CNN
dequantize, activation, next layer
Repeat per CNN layer: M / K / N reconfigured each time, edge tiles zero-padded
ARCHITECTURE
ARM Cortex-A9 (PS) control and status via AXI4-Lite | 6 interrupts
DDR3
A, B: INT8 inputs
C: INT32 results
AXI HP0
shared data path
AXI DMA 0
MM2S in / S2MM out
ENGINE 0 16 x 16 systolic mesh | 110 + 146 = 256 PEs
110
DSP48E1 MAC PEs
+
146
LUT MAC PEs
A/B staging
skew
INT8 MAC
INT20 acc
AXI DMA 1
MM2S in / S2MM out
ENGINE 1 16 x 16 systolic mesh | 110 + 146 = 256 PEs
110
DSP48E1 MAC PEs
+
146
LUT MAC PEs
A/B staging
skew
INT8 MAC
INT20 acc
Total across both engines: 220 / 220 DSP48E1 | 292 LUT-based PEs

## Slide 4
Innovation, Novelty & Value Addition
Workload adaptation
Runtime dimensions and active masks support small or irregular layers. Host tiling keeps the same hardware for larger GEMMs.
Balanced compute
110 DSP MACs in each engine plus 146 LUT MACs retain all 512 physical lanes with a symmetric allocation.
Useful on-chip storage
Two-port input banks map to BRAM. Row-enabled result reads and an elastic stream queue handle backpressure.
Measured implementation progress
Updated accelerator-only synthesis uses 38,765 LUTs versus 53,200 in the preserved baseline: 27.14% fewer LUTs.
Routed LUTs | Routed FFs | DSP48E1 | BRAM36 equivalents
38,765 / 72.86 % | 33,325 / 31.32% | 220 / 100% | 18 / 12.85%
Full-board candidate: 12,043 / 13,300 slices (90.55%); the <75% slice objective remains unmet.
Notes: Novelty here means the project implementation choices; no first-in-literature claim is made. The 12.1% reduction is (36,278 - 31,899) / 36,278, rounded to one decimal, comparing accelerator-only synthesized baseline and updated 110/110 configurations. Full-board routed numbers have a different scope and are not mixed into this percentage. Tile feeder uses eight RAMB36E1 primitives with no tile LUT RAM; result buffers use 32 RAMB18E1 primitives. Full-board total is 26 BRAM36 equivalents, including IP. Slice occupancy remains an unmet optimization objective.
Evidence inspected on October 6, 2026:
C:\Users\adars\OneDrive\Desktop\adaptive_systolic_array_docs\PYNQ-z2\results\power_optimization\README.md
C:\Users\adars\OneDrive\Desktop\adaptive_systolic_array_docs\PYNQ-z2\results\power_optimization\screen110\ooc\utilization_synth.rpt
C:\Users\adars\OneDrive\Desktop\adaptive_systolic_array_docs\PYNQ-z2\results\power_optimization\baseline
C:\Users\adars\OneDrive\Desktop\adaptive_systolic_array_docs\PYNQ-z2\results\power_optimization\dsp110_100_direct\utilization_routed.rpt
C:\Users\adars\OneDrive\Desktop\adaptive_systolic_array_docs\PYNQ-z2\src\unified_bram_feeder.sv
C:\Users\adars\OneDrive\Desktop\adaptive_systolic_array_docs\PYNQ-z2\src\c_buf.sv
C:\Users\adars\OneDrive\Desktop\adaptive_systolic_array_docs\PYNQ-z2\src\axis_out_dual_adapter.sv

## Slide 5
Software & Test Results
Test case | Size | Output vector y | Result
identity_4 | 4×4 | [3, -1, 4, 2] | ✔ PASS
zero_4 | 4×4 | [0, 0, 0, 0] | ✔ PASS
negative_4 | 4×4 | [10, 18, 26, 34] | ✔ PASS
random_4 | 4×4 | [33, 11, 51, 19] | ✔ PASS
random_8 | 8×8 | [-33, -2, -5, -111, 83, 46, 34, -64] | ✔ PASS
random_16_scalability | 16×16 | [-14, -28, 96, … 218 … -40] | ✔ PASS
max_values_4 | 4×4 | [64516, 64516, 64516, 64516] | ✔ PASS
7 / 7
test cases match expected output
4×4 → 16×16
matrix size scaled up in three steps
64,516
max-value case fits the 20-bit accumulator
Notes: Reports and logs were inspected; this presentation task did not rerun RTL or Vivado. Ten functional bench logs record PASS. tb_power_regression.txt reports 38 completed jobs and 20,239 checked words at DSP_LIMIT=110; the checked words include partial output before aborted/reset jobs. Driver metrics use a software test double, not board execution. The current dsp110_100_direct reports show complete routing and timing closure, with warnings but no critical DRCs. Vectorless dynamic power 2.428 W minus PS7 1.531 W gives a scoped 0.897 W PL estimate, excluding device static power; it does not prove the sustained <=1 W workload target. The activity manifest is smoke_only and no current-source qualified release bitstream or physical rail measurement is claimed.
Evidence inspected on October 6, 2026:
C:\Users\adars\OneDrive\Desktop\adaptive_systolic_array_docs\PYNQ-z2\results\power_optimization\regression\tb_power_regression.txt
C:\Users\adars\OneDrive\Desktop\adaptive_systolic_array_docs\PYNQ-z2\results\power_optimization\regression\driver.txt
C:\Users\adars\OneDrive\Desktop\adaptive_systolic_array_docs\PYNQ-z2\results\power_optimization\README.md
C:\Users\adars\OneDrive\Desktop\adaptive_systolic_array_docs\PYNQ-z2\results\power_optimization\dsp110_100_direct\timing_routed.rpt
C:\Users\adars\OneDrive\Desktop\adaptive_systolic_array_docs\PYNQ-z2\results\power_optimization\dsp110_100_direct\route_status.rpt
C:\Users\adars\OneDrive\Desktop\adaptive_systolic_array_docs\PYNQ-z2\results\power_optimization\dsp110_100_direct\drc.rpt
C:\Users\adars\OneDrive\Desktop\adaptive_systolic_array_docs\PYNQ-z2\results\power_optimization\dsp110_100_direct\power_vectorless.rpt
C:\Users\adars\OneDrive\Desktop\adaptive_systolic_array_docs\PYNQ-z2\results\power_optimization\dsp110_100_direct\activity_manifest.json
C:\Users\adars\OneDrive\Desktop\adaptive_systolic_array_docs\PYNQ-z2\webpage\README.md
C:\Users\adars\OneDrive\Desktop\adaptive_systolic_array_docs\PYNQ-z2\pynq\pynq_gesture_server.py

## Slide 6
Thank You
Team & Track Details
Adaptive 2D Systolic Array Matrix Accelerator
ADARSH SWARUP MAHARANA #REGD NO -2301109373
ARPITA MISHRA #REGD NO -2301109371
ASHISHAYAN PATTANYAK #REGD NO -2301109373
GHULAM QADIR #REGD NO -2301109391
SRIKANTA BEHERA #REGD NO -2301109427
Track -1 : FPGA / PYNQ-Z2 / Zynq-7000 XC7Z020
Processors - Problem #5: 2D Systolic Array-Based Processing Element
Notes: The team name NEXT IN was supplied by the user during this task. Member names and institution are deliberately editable blanks. Track and problem-statement labels come from the existing project technical report, not from an independently verified event website. The project status uses October 6 reports rather than the report's older hardware-readiness claims.
Evidence inspected on October 6, 2026:
C:\Users\adars\OneDrive\Desktop\adaptive_systolic_array_docs\Edge_AI_Hackathon_2026_Technical_Report.pdf
C:\Users\adars\OneDrive\Desktop\adaptive_systolic_array_docs\PYNQ-z2\results\power_optimization\README.md